## Slide 1
Design Overview
Spirit Electrical
Power System

## Slide 2: Design Approach
EPS Components | Mass (g) | Price ($CDN) | Dimensions (mm) | Operating Temperature | BOL Efficiency | Operating Voltage (V) | Product Link | Notes
Solar Panels | 100 | $ 5,198.66 | ~ | -40 to +125°C | 30% | 3.0 | https://www.isispace.nl/product/isis-cubesat-solar-panels/ | GaAs Triple-junction solar cells, better than Si b/c lighter, better efficiency, better resistance to radiation
 | 100 | $ 5,900.00 | 82.5 x 196 x 2.4 | -55°C to +125°C | 30% | 3.3 | https://www.cubesatshop.com/product/cubesat-solar-panels/ | Similar option but solar cells are delivered in smaller units
 | 53 | ~ | 98 x 82.6 x 9.0 | -40 to +105°C | 29.50% | 4.66 | https://www.endurosat.com/products/cubesat-solar-panels-x-y/ | 1U Solar Panel
Battery and Power Supply | 200 | $3000 - 4000 | 89.3 x 92.9 x 25.9 | -40 °C to +85 °C | 95% | 3.3 or 5.0 | https://gomspace.com/shop/subsystems/power-supplies/nanopower-p31u.aspx | Lithium-ion's key advantage or NiCa is the increased energy density and low maintenance
 | 278 | $ 3,700.00 | 90.2 x 95.9 x 30.0 | -40 to +150°C | 95% | 3.3 or 5.0 | https://www.endurosat.com/products/cubesat-power-module/ | LiPo battery with 20.8 Wh

## Slide 3: CubeSat Design Configuration

## Slide 4: CubeSat Design Configuration

## Slide 5: Power Budget
Components |  | Nominal | COMMS | Imaging | Safe | Eclipse
Subsystem | Component | Power (W) | Power (W) | Power (W) | Power (W) | Power (W)
COMM | Transmission | 0.00 | 4.95 | 0.00 | 0.00 | 0.00
 | Receiving | 1.00 | 1.00 | 0.00 | 0.00 | 0.00
subtotal |  | 1.00 | 5.95 | 0.00 | 0.00 | 0.00
C&DH | On-Board Computer | 0.55 | 0.55 | 0.55 | 0.55 | 0.55
subtotal |  | 0.55 | 0.55 | 0.55 | 0.55 | 0.55
ADCS | magnetorquer | 0.00 | 0.00 | 0.00 | 0.00 | 0.00
 | sun sensor | 0.05 | 0.05 | 0.05 | 0.00 | 0.00
 | reaction wheel | 0.00 | 2.20 | 2.20 | 0.00 | 2.20
 | Gyroscope | 0.01 | 0.01 | 0.00 | 0.00 | 0.00
subtotal |  | 0.06 | 2.26 | 2.25 | 0.00 | 2.20
payload | camera 1 | 0.00 | 0.00 | 3.00 | 0.00 | 0.00
*Voltages are estimates | camera 2 | 0.00 | 0.00 | 3.00 | 0.00 | 0.00
subtotal |  | 0.00 | 0.00 | 6.00 | 0.00 | 0.00
Power Requirement |  | 1.61 | 8.76 | 8.80 | 0.55 | 2.75
Power Consumption (Whr) |  | 2.99 | 4.78 | 2.91 | 0.83 | 2.99
*This power budget assumes an orbit of 90.0 minutes, separated into 60.0 minutes of sunlight and 30.0 minutes of eclipse. Nominal power generation at BOL is 3.1Watts in ideal conditions.

## Slide 6: Power Consumption Calculations

## Slide 7: Nominal Mode Model
Power Conditions for 1 Orbit
*These values assume ideal beginning of life conditions with 25 mins of direct sunlight, 35 mins of angled sunlight and 30 mins of eclipse*
Generation/Consumption
Net Power

## Slide 8: Safe Mode Model
Power Conditions for 1 Orbit
*These values assume ideal beginning of life conditions with 25 mins of direct sunlight, 35 mins of angled sunlight and 30 mins of eclipse*

## Slide 9: Subsystem Interaction